## Slide 1: Logic Design Project Expansion Shield for STM Nucleo

## Slide 2: Project Overview
In this project, 3 main tasks are proposed:
  Schematic design in Altium Designer
  PCB Layout and Circuit Assembly
  Device driver programming
A template for PCB design is supported for students. This template provides the interface of the shield when it is stacked in the Nucleo board (using STM32F103)
Basically, a shield is composed of LEDs, LED 7s, LED Matrixes and Buttons
A group of 2 – 3 students
  Required points = number of student * 2

## Slide 3: Digital Clock Shield (2 points)
This shield has 12 single LEDs (3mm or 5mm in size) and 3 buttons.
12 LEDs represent 12 numbers in a digital clock
1 button for mode and 2 others for up and down

## Slide 4: Two Ways Traffic Light (2 points)
This shields has 6 LEDs (for 2 way traffic light)
One LED 7 Segment for countdown number
3 buttons for mode, up and down operations

## Slide 5: LED Matrix (2 points)
1 LED matrix
2 colors (RED and GREEN)

## Slide 6: 4 LED 7s and a double dot (3 points)
4 LED 7s (to display minute and hour)
2 Single LEDs for a Dot (blink every second)
3 buttons, 1 one mode, 2 for up and down

## Slide 7: LED MATRIX with Serial connection (4 points)
Serial to parallel IC is required (MAX7219 or equivalent Ics)
Many shields can be connected to extend the size of the LED Matrix

## Slide 8: LCD 16x2 and DHT20 (6 points)
I2C connections